## Slide 1: Binary arithmetic(addition and subtraction) Complements of Numbers (r and r-1complement)

## Slide 2: Binary Addition
Basic mathematical operations with binary numbers works similar to the decimal system. However there are a few rules specific to the binary system.

## Slide 4: Binary Subtraction
Binary subtraction is also similar to that of decimal subtraction with the
difference that when 1 is subtracted from 0, it is necessary to borrow 1 from
the next higher order bit and that bit is reduced by 1 (or 1 is added to the next
bit of subtrahend) and the remainder is 1.
Binary Subtraction Rule Chart
Rules and tricks: Binary subtraction is much easier than the decimal subtraction when you remember the following rules:
0 – 0 = 0
0 – 1 = 1 ( with a borrow of 1)
1 – 0 = 1
1 – 1 = 0

## Slide 5: COMPLEMENTS OF NUMBERS
Complements are used in digital computers to simplify the subtraction operation and for logical manipulation.
Simplifying operations leads to simpler, less expensive circuits to implement the operations.
There are two types of complements for each base‐r system: the radix complement and the diminished radix complement.
The first is referred to as the r’s complement and the second as the (r - 1)’s complement.
When the value of the base r is substituted in the name, the two types are referred to as the 2’s complement and 1’s complement for binary numbers and the 10’s complement and 9’s complement for decimal numbers.

## Slide 6: Diminished Radix Complement
Given a number N in base r having n digits,
the (r - 1)’s complement of N , i.e., its diminished radix complement, is defined as (rn - 1) - N.
For decimal numbers, r = 10 and r - 1 = 9, so the 9’s complement of N is (10n - 1) - N.
In this case, 10n represents a number that consists of a single 1 followed by n 0’s.

## Slide 7: Diminished Radix Complement
10n - 1 is a number represented by n 9’s.
For example, if n = 4, we have 104 = 10,000 and 104 - 1 = 9999.
It follows that the 9’s complement of a decimal number is obtained by subtracting each digit from 9.

## Slide 8: Calculation of the 9’s complement of 546700
            999999
-546700
453299

## Slide 9: Calculation of the 9’s complement of 012398
            999999
-012398
987601

## Slide 10: Diminished Radix Complement
For binary numbers, r = 2 and r - 1 = 1, so the 1’s complement of N is (2n - 1) - N.
Again, 2n is represented by a binary number that consists of a 1 followed by n 0’s.
2n – 1 is a binary number represented by n 1’s.

## Slide 11: Diminished Radix Complement
For example, if n = 4, we have 24 = (10000)2 and 24 - 1 = (1111)2 .
Thus, the 1’s complement of a binary number is obtained by subtracting each digit from 1. However, when subtracting binary digits from 1, we can have either 1 - 0 = 1 or 1 - 1 = 0, which causes the bit to change from 0 to 1 or from 1 to 0, respectively.
Therefore, the 1’s complement of a binary number is formed by changing 1’s to 0’s and 0’s to 1’s.

## Slide 12: 1’s complement of 1011000
1 1 1 1 1 1 1
-1 0 1 1 0 0 0
0 1 0 0 1 1 1

## Slide 13: The 1’s complement of 0101101
1111111
- 0101101
1010010
The (r - 1)’s complement of octal or hexadecimal numbers is obtained by subtracting each digit from 7 or F (decimal 15), respectively.

## Slide 14: Radix Complement
The r’s complement of an n‐digit number N in base r is defined as rn - N for N ǂ 0 and as 0 for N = 0.
Comparing with the (r - 1)’s complement, we note that the r’s complement is obtained by adding 1 to the (r - 1)’s complement, since
rn - N = [(rn - 1) - N] + 1.

## Slide 15: 10’s complement of decimal 2389
Thus, the 10’s complement of decimal 2389 is 7610 + 1 = 7611 and is obtained by adding 1 to the 9’s complement value.
9999
- 2389
7610
+ 1
7611

## Slide 16: 2’s complement of binary 101100
The 2’s complement of binary 101100 is 010011 + 1 = 010100 and is obtained by adding 1 to the 1’s‐complement value.
1’s‐complement of 101100= 010011
+ 1
010100

## Slide 17: Radix Complement
Since 10n is a number represented by a 1 followed by n 0’s, 10n - N, which is the 10’s complement of N, can be formed also by leaving all least significant 0’s unchanged, subtracting the first nonzero least significant digit from 10, and subtracting all higher significant digits from 9.

## Slide 18: 10’s complement of 012398 is 987602
1000000
- 012398
987602

## Slide 19: 10’s complement of 246700 is 753300
1000000
- 246700
753300

## Slide 20
The 10’s complement of the first number is obtained by subtracting 8 from 10 in the least significant position and subtracting all other digits from 9.
The 10’s complement of the second number is obtained by leaving the two least significant 0’s unchanged, subtracting 7 from 10, and subtracting the other three digits from 9.
Similarly, the 2’s complement can be formed by leaving all least significant 0’s and the first 1 unchanged and replacing 1’s with 0’s and 0’s with 1’s in all other higher significant digits.

## Slide 21: Obtain 2’s complement of the binary number 1101100
1’s complement of 1101100=0010011
2’s complement of 1101100= 1’s complement of 1101100+1
= 0010011
+ 1
= 0010100

## Slide 22: Obtain 2’s complement of the binary number 0110111
1’s complement of 0110111 =1001000
2’s complement of 0110111 = 1’s complement of 0110111 +1
= 1001000
+ 1
= 1001001

## Slide 23
The 2’s complement of the first number is obtained by leaving the two least significant 0’s and the first 1 unchanged and then replacing 1’s with 0’s and 0’s with 1’s in the other four most significant digits.
The 2’s complement of the second number is obtained by leaving the least significant 1 unchanged and complementing all other digits.

## Slide 24
It is also worth mentioning that the complement of the complement restores the number to its original value .
To see this relationship, note that the r’s complement of N is rn - N, so that the complement of the complement is
rn - (rn - N) = N and is equal to the original number.

## Slide 25: Assignment
1. Add and multiply the following numbers without converting them to decimal.
(a) Binary numbers 1011 and 101.
(b) Hexadecimal numbers 2E and 34.
2. Obtain the 1’s and 2’s complements of the following binary numbers:
(a) 00010000 (b) 00000000
(c) 11011010 (d) 10101010
(e) 10000101 (f) 11111111.

## Slide 26
3. Find the 9’s and the 10’s complement of the following
decimal numbers:
(a) 25,478,03 (b) 63, 325, 600
(c) 25,000,000 (d) 00,000,000.
4. (a) Find the 16’s complement of C3DF.
(b) Convert C3DF to binary.
(c) Find the 2’s complement of the result in (b).
(d) Convert the answer in (c) to hexadecimal and
compare with the answer in (a).