## Slide 1: Digital Logic
Lecture 1
Introduction

## Slide 2: Book
Digital Design: With an Introduction to the Verilog HDL, VHDL, and System Verilog, 6th Edition M. Morris R. Mano

## Slide 3: Mark Distribution
This subject comes under grading pattern 1 and follows Relative Grading System.
Mark Distribution(Total Mark= 100)
Attendance : 5 Marks
Major Lab / Session Assignments / Quizzes : 10 Marks
Minor Assignments : 10 Marks
Mid-term Examination : 15 Marks
Total Internal : 40 Marks
In-Lab Examination : 15 Marks
Theory Examination : 45 Marks
Total External : 60 Marks

## Slide 4: Contents
Digital Systems and Binary Numbers
Boolean Algebra and Logic Gates
Gate‐Level Minimization
Combinational Logic
Synchronous Sequential Logic
Registers and Counters
Memory and Programmable Logic
Design at the Register Transfer Level

## Slide 5: Digital Systems and Binary Numbers
This topic presents the various binary systems suitable for representing information in digital systems.
The binary number system is explained and binary codes are illustrated.
Examples are given for addition and subtraction of binary numbers and decimal numbers in binary‐coded decimal (BCD) format.

## Slide 6: Boolean Algebra and Logic Gates
This topic introduces the basic postulates of Boolean algebra and shows the correlation between Boolean expressions and their corresponding logic diagrams.
All possible logic operations for two variables are investigated, and the most useful logic gates used in the design of digital systems are identified.
This topic also introduces basic CMOS logic gates.

## Slide 7: Gate‐Level Minimization
This topic covers the map method for simplifying Boolean expressions.
The map method is also used to simplify digital circuits constructed with AND‐OR, NAND, or NOR gates.
All other possible two‐level gate circuits are considered, and their method of implementation is explained.
Verilog HDL is introduced together with simple examples of gate‐level models.

## Slide 8: Combinational Logic
This topic outlines the formal procedures for the analysis and design of combinational circuits.
Some basic components used in the design of digital systems, such as adders and code converters, are introduced as design examples.
Frequently used digital logic functions such as parallel adders and subtractors, decoders, encoders, and multiplexers are explained, and their use in the design of combinational circuits is illustrated.
HDL examples are given in gate‐level, dataflow, and behavioral models to show the alternative ways available for describing combinational circuits in Verilog HDL.

## Slide 9: Synchronous Sequential Logic
This topic outlines the formal procedures for analyzing and designing clocked (synchronous) sequential circuits.
The gate structure of several types of flip‐flops is presented together with a discussion on the difference between level and edge triggering.
Specific examples are used to show the derivation of the state table and state diagram when analyzing a sequential circuit.
A number of design examples are presented with emphasis on sequential circuits that use D‐type flip‐flops.
Behavioral modeling in Verilog HDL for sequential circuits is explained. HDL Examples are given to illustrate Mealy and Moore models of sequential circuits.

## Slide 10: Registers and Counters
This topic deals with various sequential circuit components such as registers, shift registers, and counters.
These digital components are the basic building blocks from which more complex digital systems are constructed.
HDL descriptions of shift registers and counter are presented.

## Slide 11: Memory and Programmable Logic
This topic deals with random access memory (RAM) and programmable logic devices.
Memory decoding and error correction schemes are discussed.
Combinational and sequential programmable devices such as ROMs, PLAs, and PALs are presented.

## Slide 12: Design at the Register Transfer Level
This topic deals with the register transfer level (RTL) representation of digital systems with example.

## Slide 13
Lesson Plan
Lecture Number | Topic
Lecture 1 | Introduction to the course & Digital Systems
Lecture 2 | Number System: Number Base Conversions Decimal to other number system conversion and vice versa Binary to Octal Binary to Hexadecimal
Lecture 3 | Binary arithmetic(addition and subtraction) Complements of Numbers (r and r-1complement)
Lecture 4 | Subtraction using complement (1s&2s)
Lecture 5 | Binary Codes
Lecture 6 | Boolean Algebra & Logic Gates: Basic Definitions, Basic Theorems and Properties of Boolean Algebra
Lecture 7 | Boolean functions, Simplification of Boolean functions using Boolean Algebra rules
Lecture 8 | Introduction to Hardware Description Language(Gate-level modeling, Dataflow modeling, Behavioral modeling)
Lecture 9 | Complement of Boolean Function, canonical and standard form, HDL Description of Boolean Functions
Lecture 10 | Other Logic operations, Digital Logic gates, Integrated Circuits

## Slide 14
Lecture Number | Topic
Lecture 11 | Gate Level Minimization Simplification of Boolean functions using Map method ( Two and Three variable map methods), HDL Description of Simplified Boolean Functions
Lecture 12 | Simplification of Boolean functions: 4 variable maps, Concept of 5 and 6 variable map, HDL Description of Simplified Boolean Functions
Lecture 13 | Simplification of Boolean functions using K map with don’t care conditions, HDL Description of Simplified Boolean Functions
Lecture 14 | SOP & POS implementation using NAND & NOR gates, HDL Description of the circuit.
Lecture 15 | Multilevel NAND, NOR circuits, Exclusive OR and Equivalence Functions, HDL Description of the circuit.
Lecture 16 | Introduction to Combinational Logic- Combinational circuit analysis and design procedure, HDL Description of the circuit
Lecture 17 | Binary Adder, HDL Models for Adder
Lecture 18 | Binary Subtractor, HDL Models for Subtractor
Lecture 19 | Code conversion and Analysis Procedure
Lecture 20 | Binary Parallel adder, HDL Models for Binary Parallel Adder
Lecture 21 | Decimal Adder, Magnitude Comparator, HDL Models of Magnitude Comparator
Lecture 22 | Decoders, Combinational Logic design using Decoders, Encoders HDL Models for Combinational Circuits (Decoder, Encoder)

## Slide 15
Lecture Number | Topic
Lecture 23 | Multiplexers, Combinational Logic design using Multiplexers
Lecture 24 | HDL Models for Combinational Circuits using Multiplexer
Lecture 25 | Introduction to Sequential Circuits, Storage Elements: Latches, HDL Description of Latch
Lecture 26 | Storage Elements: Flip Flops RS flip-flop (Graphical Symbol, Logic Diagram, Function Table, Characteristics Table, Characteristics Equation, Excitation table) HDL Description of RS Flip Flop
Lecture 27 | Storage Elements: Flip Flops JK flip-flop (Graphical Symbol, Logic Diagram, Function Table, Characteristics Table, Characteristics Equation, Excitation table) HDL Description of JK Flip Flop
Lecture 28 | Storage Elements: Flip Flops D and T flip-flop (Graphical Symbol, Logic Diagram, Function Table, Characteristics Table, Characteristics Equation, Excitation table) HDL Description of Flip Flops
Lecture 29 | Master-slave Flip Flop, Analysis of clocked Sequential Circuits
Lecture 30 | Analysis of clocked Sequential Circuits contd.
Lecture 31 | State Reduction and Assignment
Lecture 32 | Design Procedure of clocked sequential circuit
Lecture 33 | Register, Shift Registers, HDL Models for Shift Register
Lecture 34 | Design of Ripple Counters with timing sequences

## Slide 16
Lecture Number | Topic
Lecture 35 | Design of Synchronous counters,
Lecture 36 | Design of Synchronous counters contd.
Lecture 37 | Design of Synchronous counters contd.
Lecture 38 | HDL Models for Counters
Lecture 39 | Memory : Random Access Memory, Read Only Memory, Programmable Logic Array, Programmable Array Logic, HDL Description for Read and write operations of memory
Lecture 40 | Introduction to Register Transfer Level(RTL)

## Slide 17: DIGITAL SYSTEMS
Digital systems have such a prominent role in everyday life that we refer to the present technological period as the digital age.
Digital systems are used in communication, business transactions, traffic control, spacecraft guidance, medical treatment, weather monitoring, the Internet, and many other commercial, industrial, and scientific enterprises.
We nave digital telephones, digital televisions, digital versatile discs, digital cameras, handheld devices, and, of course, digital computers.

## Slide 18
We enjoy music downloaded to our portable media player (e.g., iPod Touch™) and other handheld devices having high resolution displays.
These devices have graphical user interfaces (GUIs), which enable them to execute commands that appear to the user to be simple, but which, in fact, involve precise execution of a sequence of complex internal instructions.
Most, if not all, of these devices have a special‐purpose digital computer embedded within them.

## Slide 19
The most striking property of the digital computer is its generality. It can follow a sequence of instructions, called a program, that operates on given data.
The user can specify and change the program or the data according to the specific need.
Because of this flexibility, general‐purpose digital computers can perform a variety of information processing tasks that range over a wide spectrum of applications.

## Slide 20
One characteristic of digital systems is their ability to represent and manipulate discrete elements of information.
Any set that is restricted to a finite number of elements contains discrete information. Examples of discrete sets are the 10 decimal digits, the 26 letters of the alphabet, the 52 playing cards, and the 64 squares of a chessboard.
Early digital computers were used for numeric computations. In this case, the discrete elements were the digits.
From this application, the term digital computer emerged.

## Slide 21
Discrete elements of information are represented in a digital system by physical quantities called signals.
Electrical signals such as voltages and currents are the most common.
Electronic devices called transistors predominate in the circuitry that implements these signals.
The signals in most present‐day electronic digital systems use just two discrete values and are therefore said to be binary.
A binary digit, called a bit, has two values: 0 and 1. Discrete elements of information are represented with groups of bits called binary codes.

## Slide 22
Through various techniques, groups of bits can be made to represent discrete symbols, not necessarily numbers, which are then used to develop the system in a digital format.
Thus, a digital system is a system that manipulates discrete elements of information represented internally in binary form.
In today’s technology, binary systems are most practical because, as we will see, they can be implemented with electronic components.

## Slide 23: Example of digital system
The general‐purpose digital computer is the best‐known example of a digital system.
The major parts of a computer are a memory unit, a central processing unit, and input–output units.
The memory unit stores programs as well as input, output, and intermediate data.
The central processing unit performs arithmetic and other data‐processing operations as specified by the program.

## Slide 24
The program and data prepared by a user are transferred into memory by means of an input device such as a keyboard.
An output device, such as a printer, receives the results of the computations, and the printed results are presented to the user.
A digital computer can accommodate many input and output devices.
One very useful device is a communication unit that provides interaction with other users through the Internet.
A digital computer is a powerful instrument that can perform not only arithmetic computations, but also logical operations. In addition, it can be programmed to make decisions based on internal and external conditions.

## Slide 25: Why commercial products are made with digital circuits ?
Like a digital computer, most digital devices are programmable.
By changing the program in a programmable device, the same underlying hardware can be used for many different applications, thereby allowing its cost of development to be spread across a wider customer base.

## Slide 26
As the number of transistors that can be put on a piece of silicon increases to produce complex functions, the cost per unit decreases and digital devices can be bought at an increasingly reduced price.
Equipment built with digital integrated circuits can perform at a speed of hundreds of millions of operations per second.
Digital systems can be made to operate with extreme reliability by using error‐correcting codes.
An example of this strategy is the digital versatile disk (DVD), in which digital information representing video, audio, and other data is recorded without the loss of a single item.

## Slide 27
A digital system is an interconnection of digital modules.
To understand the operation of each digital module, it is necessary to have a basic knowledge of digital circuits and their logical function.

## Slide 28: Why we should learn HDL?
we note that industry has largely abandoned schematic‐based design entry, a style which emerged in the 1980s, during the nascent development of CAD tools for integrated circuit (IC) design.
Schematic entry creates a representation of functionality that is implicit in the layout of the schematic.
Unfortunately, it is difficult for anyone in a reasonable amount of time to determine the functionality represented by the schematic of a logic circuit without having been instrumental in its construction, or without having additional documentation expressing the design intent.
Consequently, industry has migrated to HDLs (e.g., Verilog) to describe the functionality of a design and to serve as the basis for documenting, simulating, testing, and synthesizing the hardware implementation of the design in a standard cell‐based ASIC or an FPGA.

## Slide 29: Why we should learn HDL?
The utility of a schematic depends on the careful, detailed documentation of a carefully constructed hierarchy of design modules.
In the old paradigm, designers relied upon their years of experience to create a schematic of a circuit to implement functionality.
In today’s design flow, designers using HDLs can express functionality directly and explicitly, without years of accumulated experience, and use synthesis tools to generate the schematic as a byproduct, automatically.
Industry practices arrived here because schematic entry dooms us to inefficiency, if not failure, in understanding and designing large, complex ICs.

## Slide 30
In this course we will try to give emphasis on how hardware is designed, to better prepare a student for a career in today’s industry, where HDL‐based design practices are dominant.
Xilinx ISE